//****************************************************************//

//	              Program for AM230x series

//MCU：  AT89S52 ,   Frequency of crystal oscillator: 11.0592MHz

//Function： Transmit RH & Temp. Data via PC interface ,  Baud rate 9600

//Connection： P2.0 connected with DHT sensor

// Company  ： Aosong Electronics

//****************************************************************//

#include <reg51.h>

#include <intrins.h>

//

typedef unsigned char  U8;       /* defined for unsigned 8-bits integer variable 	     */

typedef signed   char  S8;       /* defined for signed 8-bits integer variable		   */

typedef unsigned int   U16;      /* defined for unsigned 16-bits integer variable 	     */

typedef signed   int   S16;      /* defined for signed 16-bits integer variable 	     */

typedef unsigned long  U32;      /* defined for unsigned 32-bits integer variable 	  */

typedef signed   long  S32;      /* defined for signed 32-bits integer variable 	      */

typedef float          F32;      /* single precision floating point variable (32bits)    */

typedef double         F64;      /* double precision floating point variable (64bits)    */

//

#define uchar unsigned char

#define uint unsigned int

#define   Data_0_time    4

//----------------------------------------------//

//----------------Definition for IO interface--------------------//

//----------------------------------------------//

sbit  P2_0  = P2^0 ;

sbit  P2_1  = P2^1 ;

sbit  P2_2  = P2^2 ;

sbit  P2_3  = P2^3 ;

//----------------------------------------------//

//----------------Definition zone--------------------//

//----------------------------------------------//

U8  U8FLAG,k;

U8  U8count,U8temp;

U8  U8T_data_H,U8T_data_L,U8RH_data_H,U8RH_data_L,U8checkdata;

U8  U8T_data_H_temp,U8T_data_L_temp,U8RH_data_H_temp,U8RH_data_L_temp,U8checkdata_temp;

U8  U8comdata;

U8  outdata[5];

U8  indata[5];

U8  count, count_r=0;

U8  str[5]={"RS232"};

U16 U16temp1,U16temp2;

SendData(U8 *a)

{

outdata[0] = a[0];

outdata[1] = a[1];

outdata[2] = a[2];

outdata[3] = a[3];

outdata[4] = a[4];

count = 1;

SBUF=outdata[0];

}

void Delay(U16 j)

{      U8 i;

for(;j>0;j--)

{

for(i=0;i<27;i++);

}

}

void  Delay_10us(void)

{

U8 i;

i--;

i--;

i--;

i--;

i--;

i--;

}

void  COM(void)

{

U8 i;

for(i=0;i<8;i++)

{

U8FLAG=2;

while((!P2_0)&&U8FLAG++);

Delay_10us();

Delay_10us();

Delay_10us();

U8temp=0;

if(P2_0)U8temp=1;

U8FLAG=2;

while((P2_0)&&U8FLAG++);

if(U8FLAG==1)break;

U8comdata<<=1;

U8comdata|=U8temp;        //0

}//rof

}

//--------------------------------

//-----Sub-program for reading %RH ------------

//--------------------------------

//----All the variable bellow is global variable--------

//----Temperature's high 8bit== U8T_data_H------

//----Temperature's low 8bit== U8T_data_L------

//----Humidity's high 8bit== U8RH_data_H-----

//----Humidity's low 8bit== U8RH_data_L-----

//----Check-sum 8bit == U8checkdata-----

//--------------------------------

void RH(void)

{

P2_0=0;

Delay(5);

P2_0=1;

Delay_10us();

Delay_10us();

Delay_10us();

Delay_10us();

P2_0=1;

if(!P2_0)

{

U8FLAG=2;

while((!P2_0)&&U8FLAG++);

U8FLAG=2;

while((P2_0)&&U8FLAG++);

COM();

U8RH_data_H_temp=U8comdata;

COM();

U8RH_data_L_temp=U8comdata;

COM();

U8T_data_H_temp=U8comdata;

COM();

U8T_data_L_temp=U8comdata;

COM();

U8checkdata_temp=U8comdata;

P2_0=1;

U8temp=(U8T_data_H_temp+U8T_data_L_temp+U8RH_data_H_temp+U8RH_data_L_temp);

if(U8temp==U8checkdata_temp)

{

U8RH_data_H=U8RH_data_H_temp;

U8RH_data_L=U8RH_data_L_temp;

U8T_data_H=U8T_data_H_temp;

U8T_data_L=U8T_data_L_temp;

U8checkdata=U8checkdata_temp;

}//fi

}//fi

}

//----------------------------------------------

//               main()

//----------------------------------------------

void main()

{

U8  i,j;

TMOD = 0x20;

TH1 = 253;

TL1 = 253;

TR1 = 1;

SCON = 0x50;

ES = 1;

EA = 1;

TI = 0;

RI = 0;

SendData(str) ;

Delay(1);

while(1)

{

//------------------------

//调用温湿度读取子程序

RH();

//--------------------------

str[0]=U8RH_data_H;

str[1]=U8RH_data_L;

str[2]=U8T_data_H;

str[3]=U8T_data_L;

str[4]=U8checkdata;

SendData(str) ;

Delay(20000);

}//elihw

}// main

void RSINTR() interrupt 4 using 2

{

U8 InPut3;

if(TI==1)

{

TI=0;

if(count!=5)

{

SBUF= outdata[count];

count++;

}

}

if(RI==1)

{

InPut3=SBUF;

indata[count_r]=InPut3;

count_r++;

RI=0;

if (count_r==5)

{

count_r=0;

str[0]=indata[0];

str[1]=indata[1];

str[2]=indata[2];

str[3]=indata[3];

str[4]=indata[4];

P0=0;

}

}

}